## Slide 1: SNMP (Simple Network Management Protocol) Overview
Draft Version

## Slide 2
Simple Network Management Protocol (SNMP)
Ethernet is not a supervised protocol
SNMP provides a method to monitor the status, connection and communication of devices on a LAN
Uses
  Traps (notification of events)
  Sets (configuration and control)
  Gets (retrieves data)
  Management Information Base (MIB’s) (device data structure)
  Community strings (text strings like passwords)
SNMP Overview

## Slide 3
SNMP-enabled Switch
IP Camera
IT Mgr’s PC
with SNMP manager
2. “Trap” message sent to monitoring computer
X
3. Monitoring software can generate screen messages, email alerts, other annunciations
1. Device connection or power fails
SNMP Example

## Slide 4
Gets retrieve information
Traps notify of events
Sets configure and control
Manager – server running processes to receive or modify information in the device
Agents – software running on the device; talks to the Manager
SNMP (Simple Network Management Protocol) – defines:
  communication rules between SNMP-capable devices
  message types
MIB (Management Information Base) – a database of objects in the device tracked by the agent
SMI (Structure of Management Information) – how information is organized
  Numerical hierarchy of MIB’s
SNMP Overview

## Slide 5
Graphic courtesy of Microsoft Corporation

## Slide 6
Define the information that can be retrieved or altered in a device
“Standard” MIB’s are well defined and vetted
  Documented in RFC’s (Request for Comments)
  Typically proposed by standards organizations
“Enterprise” MIB’s are unique to an organization
  Enterprises are assigned numbers by IANA
MIB’s known categorized by Object Identifier (OID)
  In enterprise MIB’s, enterprise number is part of the OID
MIB’s

## Slide 7
MIB OID Hierarchy

## Slide 8
SNMPv1 (1988) – Initial implementation
  Poor security
  Used “Community Strings” as surrogates for passwords
  SNMPv2c - Most popular version of SNMPv2 (1999)
  Widely used
  Maintains community strings for security
  RFC 2578
SNMPv3 (2002) – Added cryptographic security
  Most secure version if features are used
  RFC 3414
SNMP Versions

## Slide 10
Encryption Options
Axis

## Slide 11
Samsung

## Slide 12
ISOC – The Internet Society
  IETF – Internet Engineering Task Force
    IAOC – IETF Administrative Oversight Committee
    IAB – Internet Architecture Board
      RSOC – RFC Oversight Committee
  IESG – Internet Engineering Steering Group
  IRTF – Internet Research Task Force
ICANN - Internet Corporation for Assigned Names and Numbers
  IANA – Internet Assigned Numbers Authority
RSE – RFC Series Editor (independent)
  http://www.rfc-editor.org/rse/
Who Controls the Process?

## Slide 13
www.internetsociety.org
“an international, non-profit, membership organization that fosters the expansion of the Internet”
Organizational home for:
  Internet Architecture Board (IAB)
  Internet Engineering Task Force (IETF)
  Internet Engineering Steering Group (IESG)
  Internet Research Task Force (IRTF)
ISOC
The Internet Society

## Slide 14
www.ietf.org
“The mission of the IETF is to make the Internet work better by producing high quality, relevant technical documents that influence the way people design, use, and manage the Internet”
  actions associated with entry into and movement along the Internet "standards track" including final approval of specifications as Internet Standards and publication as an RFC
Supervises the IETF Administrative Oversight Committee (IAOC)
Good reference: http://www.ietf.org/tao.html
IETF
The Internet Engineering Task Force

## Slide 15
www.iab.org
  A committee of the IETF
Architectural Oversight
Standards Process Oversight and Appeal
Editorial management and publication of RFC’s
RSOC - RFC Series Oversight Committee
IAB
The Internet Architecture Board

## Slide 16
www.ietf.org/iesg.html
Composed of IETF Area Directors
Responsible for technical management of IETF activities and the Internet standards
Ratifies or steers the output from the IETF's Working Groups (WGs)
Gets WGs started and finished
Makes sure that non-WG drafts that are about to become RFCs are correct.
IESG
Internet Engineering Steering Group

## Slide 17
www.icann.org
Coordinates a select set of the Internet's technical management functions, such as
  the assignment of protocol parameters
  the management of the domain name system
  the allocation of Internet protocol (IP) address space,
  management of the root server system.
Coordinates IANA activities
Defines policies for Internet names and numbers
Revenues derived from DNS registrations
ICANN
Internet Corporation for Assigned Names and Numbers

## Slide 18
www.iana.org
“allocates and maintains unique codes and numbering systems that are used in the technical standards (“protocols”) that drive the Internet”
    Domain names
    Number resources
    Protocol assignments (numbering systems)
IANA
The Internet Assigned Numbers Authority

## Slide 19
www.rfc-editor.org/rse
The "RFC Editor" comprises the set of functions that serve the Internet technical community in editing, publishing, and archiving RFCs.
RSE directs the work of the RFC Editor
See RFC 6635 (http://tools.ietf.org/html/rfc6635)
RFC Series Editor
RSE

## Slide 20
ISOC
  IAB
    RSOC
  IETF
    IAOC
  IESG
  IRTF
    IRSG
Ruling Organizations
ICANN
  IANA
RFC Series Editor (RSE)

## Slide 22
Memoranda describing methods, behaviors, research, or innovations
IETF official publication channel
Means for soliciting feedback
Path for a proposal to become a standard
RFC‘s cover standard MIB’s
Usually the result of a Working Group effort
RFC’s – Requests for Comments